## Slide 1: Environmental Chemistry
IB Option E Part 2: Smog, Greenhouse Effect & Ozone Depletion

## Slide 2: AIR POLLUTION
Some primary air pollutants may react with one another or with other chemicals in the air to form secondary air pollutants.

## Slide 3: SMOG
Two types:
  Oxidizing smog: “photochemical smog” – result of NOX rxns in the presence of UV light (occurs in dry sunshine). This is responsible for the brown cloud of LA.
Link to NASA’s AURA data
Los Angeles
Population density
Jan 2011 NO2

## Slide 4: SMOG
Two types:
  Reducing smog: “pea soup smog” – result of carbon particulates and sulfur dioxide (occurs in cold, damp weather). Creates yellow-green smog --- due to env. controls, largely a thing of the past (thank goodness!!!)
London Fog

## Slide 5: NUCLEAR ENERGY- Dream or Dilusion???

## Slide 6: NUCLEAR ENERGY- Dream or Dilusion???

## Slide 7: Nuclear Energy
Clean air, but in light of recent events in Japan, is this really a good alternative???

## Slide 8: Thermal Inversions: occur when the normal temperature gradient is reversed (temp.  with altitude).
tropospheric altitude
temperature
tropospheric altitude
temperature
Normal Conditions: temp. decreases by  1C / 100 m of increasing altitude in dry tropospheric air
Thermal Inversion: layer of warm air becomes trapped, capping cool air near the surface

## Slide 9: Thermal Inversions
Cold, cloudy weather in a valley surrounded by mountains can trap air pollutants (left).
Areas with sunny climate, light winds, mountains on three sides and an ocean on the other (right) are susceptible to inversions.
Denver
LA

## Slide 10: Thermal Inversion Demonstration

## Slide 11: Thermal Inversion
Normal conditions
Thermal inversion

## Slide 12: Thermal Inversions
Occur in bowl-shaped cities when it is warm and dry and there is no wind.

## Slide 13: Thermal Inversions
Mountains, buildings and other barriers around cities can also promote the development of thermal inversions by preventing horizontal movement of air.

## Slide 14: Thermal Inversions
Under these conditions, warm air caps/traps pollutants.

## Slide 15: Photochemical Smog
Today’s air pollution problem
Caused by traffic exhaust fumes
Free radical rxns between sunlight, NOx and VOC’s

## Slide 16: Ozone, O3 (GOOD up high, BAD nearby)
Mechanism (know):
  N2 + O2  2NO
  2NO + O2  2NO2 (brown)
  NO2 + sunlight (UV)  NO + O
  O2 + O  O3

## Slide 17: Tropospheric Ozone
Yes, a problem HERE
Link to Ozone GIS

## Slide 18: Daily pollution fluctuations

## Slide 19: Peroxyacylnitrates, (PANs)
Secondary pollutants that are eye irritants

## Slide 20: What is a peroxide?
Compound containing an O-O single bond or the peroxide anion (O-O)2-.
Here’s a fun one: ascaridole – a bicyclic monoterpene found in Mexican tea

## Slide 21: Peroxyacylnitrates, (PANs)
Mechanism (know): Production of hydrocarbon radicals:
  RH + O  R + OH
  alkyl radicals and hydroxyl radicals produced when VOCs are oxidized
  RCH3 + OH  RCH2 + H2O
  hydroxyl radicals react with alkanes to produce further alkyl radicals
  RCH2 + O2  RCH2O2
  these alkyl radicals react with O2 molecules to produce peroxy radicals

## Slide 22: Peroxyacylnitrates, (PANs)
  Mechanism (know): Production of aldehydes:
    RCH2O2 + NO  RCH2O + NO2
    peroxy radicals react with nitrogen monoxide to produce nitrogen dioxide
    RCH2O + O2  RCHO + HO2
      RCH2O radicals react with oxygen to form aldehydes

## Slide 23: Peroxyacylnitrates, (PANs)
  Mechanism (know): Production of PANs by hydroxyl radicals and aldehydes
    RCHO + OH  RCO + H2O
    H-atom is removed from an aldehyde
    RCO + O2  RCOOO
    resulting radical reacts with oxygen molecule to produce a peroxide
    Termination step:
    free radicals (above) + NO  PAN
    (relatively stable)

## Slide 24: Greenhouse Effect
Greenhouse gases allow the passage of incoming solar short-wavelength radiation but absorb the longer-wavelength radiation from the Earth. Some of the absorbed radiation is re-radiated back to Earth.

## Slide 25: Major greenhouse gases
H2O
CO2
CH4
N2O
O3
CFCs

## Slide 26: Table 2: Major greenhouse gases you should know
Gas | Main Source | Heat Trapping Effectiveness Compared With CO2 | Overall contribution to increased global warming
H2O | Evaporation of oceans | 0.1 | -
CO2 | Combustion of fossil fuels and biomass | 1 | 50%
CH4 | Anaerobic decay of organic matter caused by intensive farming | 30 | 18%
N2O | Artificial fertilizers and combustion of biomass | 150 | 6%
O3 | Secondary pollutant in photochemical smog | 2000 | 12%
CFCs | Refrigerants, propellants, foaming agents, solvents | 10,000-25,000 | 14%

## Slide 27: Effects of increasing amounts of greenhouse gases on the atmosphere:
Rising sea-levels (from thermal expansion of oceans and melting of the polar ice-caps)

## Slide 28: Effects of increasing amounts of greenhouse gases on the atmosphere:
Rising sea-levels (from thermal expansion of oceans and melting of the polar ice-caps)

## Slide 29: Effects of increasing amounts of greenhouse gases on the atmosphere:
Rising sea-levels (from thermal expansion of oceans and melting of the polar ice-caps)

## Slide 30: Effects of increasing amounts of greenhouse gases on the atmosphere:
Changes in precipitation and temperature of regions (causing floods and droughts)

## Slide 31: Effects of increasing amounts of greenhouse gases on the atmosphere:
Changes in yield and distribution of commercial crops

## Slide 32: Effects of increasing amounts of greenhouse gases on the atmosphere:
Changes in yield and distribution of commercial crops

## Slide 33: Effects of increasing amounts of greenhouse gases on the atmosphere:
Changes in distribution of pests and disease-carrying organisms

## Slide 35: Stratospheric Ozone
Good up high! (Absorbs dangerous UV-C)

## Slide 36: Stratospheric Ozone
Table 3: Formation and depletion of stratospheric ozone by natural processes
Formation | Depletion
O2 + UV (<242 nm) → 2O O2 + O → O3 | O3 + UV (<330 nm) → O2 + O O3 + O→ 2O2

## Slide 37: Stratospheric Ozone
Table 3: Formation and depletion of stratospheric ozone by natural processes
Formation | Depletion
O2 + UV (<242 nm) → 2O O2 + O → O3 | O3 + UV (<330 nm) → O2 + O O3 + O→ 2O2
Shorter wavelength, thus higher energy
Longer wavelength, thus lower energy
Stronger bond to break
Weaker bond to break

## Slide 38: Ozone thinning problem

## Slide 39: Stratospheric Ozone Depletion
Table 4: Mechanisms for ozone depletion by anthropogenic sources
Catalyst | Source | Sample Mechanism (know these) | Net Effect
CFCs (most common = CCl2F2, a.k.a. Freon or CFC-12) | Refrigerants, propellants for aerosols, foaming agents for expanding plastics and cleaning solvents | CCl2F2 → CClF2 + Cl Cl + O3 → ClO + O2 ClO + O → O2 + Cl | O3 + O → 2O2

## Slide 40
Table 4: Mechanisms for ozone depletion by anthropogenic sources
Catalyst | Source | Sample Mechanism (know these) | Net Effect
NOX | High temperatures inside combustion engines, power stations and jet aeroplanes. | NO + O3 → NO2 + O2 NO2 + O → NO + O2 | O3 + O → 2O2
Stratospheric Ozone Depletion

## Slide 41: Alternatives to CFCs
Alternatives to CFCs for the future should have the following characteristics:
  Similar properties to CFC’s, but
    Low reactivity
    Low toxicity
    Low flammability
    No weak C-Cl bonds that can easily be broken by UV to form radicals
    Inability to absorb infrared radiation
      (not greenhouse gases)

## Slide 42: Alternatives to CFCs

## Slide 43: Table 5: Most immediate replacements
Class of chemicals | Lewis structure of example | Benefits | Drawbacks
HCFCs | Chlorodifluormethane | Decompose more readily than CFCs and do not build up in stratosphere | Still contains one C-Cl bond per molecule
HFCs | 1,1,1,2-tetrafluoroethane | Good refrigerant | Flammable Greenhouse gases
hydrocarbons | 2-methylpropane | Good refrigerant | Flammable Greenhouse gases

## Slide 44: Greatest ozone depletion occurs in polar regions:
Very low temperatures in winter
Small amounts of water vapor in air freezes to form ice crystals.
Crystals also contain small amounts of molecules, such as HCl and ClONO2.
Catalytic rxns occur on the surface of the ice crystals to produce species such as hypochlorous acid (HClO) and chlorine (Cl2).

## Slide 45: Greatest ozone depletion occurs in polar regions:
Each spring, the Sun causes these molecules to break down, giving off Cl radicals.
These Cl radicals catalyze the destruction of ozone.

## Slide 46: Greatest ozone depletion occurs in polar regions:
Largest ozone layer holes occur during early spring.
As Sun continues to warm the air, ice crystals disperse and ozone concentrations gradually increase again.

## Slide 47: How does sunscreen work?
Contain conjugated unsaturated hydrocarbons (organic compounds) that absorb in the UV region.
  e.g. para-aminobenzonic acid (PABA)

## Slide 48: How does sunblock work?
Sunblock (e.g. zinc oxide), on the other hand, is just an opaque white inorganic solid substance that blocks out the sun entirely (reflects all UV and visible light).