## Slide 1: Analytical Chemistry
Option A
Part 3: AA and Chromatography

## Slide 2: Atomic Absorption (AA)

## Slide 3: Atomic Absorption (AA)
Measures energy absorbed as electrons are promoted to higher energy level.
Extremely sensitive – measures concentrations as low as 1 ppb
Used to measure concentrations of metals in water, blood, soils, etc.

## Slide 4: AA – How it Works

## Slide 5: AA – How it Works

## Slide 6: Analyzing AA Spectra
Recall that Beer-Lambert’s law only applies strictly to dilute sol’ns, so it is not generally used directly.
In practice, known concentrations are used to produce calibration curves.
Absorbance of unknown is then measured and concentration can be read by interpolation of the calibration curve.

## Slide 7: Chromatography

## Slide 8: Chromatography
A technique for separating and identifying components in a mixture.
Components have different affinities for two phases: a stationary phase and a mobile phase
A component which has a strong attraction for the mobile phase will move quickly, while a component with a strong attraction for the stationary phase will be held back.

## Slide 9: Chromatography
Stationary and mobile phases are carefully selected so that the different components of the mixture will move at different speeds and thus be separated effectively.
For example, if the stationary phase is nonpolar and a polar mobile phase is employed, components will separate out based on their relative polarities (most polar will travel fastest).

## Slide 10: Partition chromatography
Non-volatile liquid stationary phase
Inert solid surface
Components distribute themselves between the two phases according to their relative solubility.
Most soluble = fastest
Examples: Paper, GLC and TLC

## Slide 11: Adsorption chromatography
Solid stationary phase
Mobile liquid or gas phase
Components distribute themselves between the two phases according to their relative polarity.
Most polar = fastest (if stationary phase is a polar solid)
Example: LC, HPLC and at times TLC

## Slide 12: Main types of chromatography
Paper chromatography
Thin layer chromatography (TLC)
Column chromatography
Gas-liquid chromatography (GLC)
Gas chromatography – mass spectrometry (GCMS)
High Performance Liquid Chromatography (HPLC)

## Slide 13: Paper chromatography
Paper composed mostly of cellulose.
Polar due to hydroxyl groups
“Dry” paper is actually ~10% water (H-bonded to –OH) groups
  Polar water bonded to paper = stationary phase
  Added solvent (eluent) = mobile phase

## Slide 14: Paper chromatography
Small amt. mixture spotted onto paper
Starting point marked
Paper suspended in small quantity of solvent (eluent)
Closed container (prevents solvent evaporation & speeds process)
As solvent rises, components partition between two phases bases on relative solubility.
Solvent front is marked at end of separation
Colored components can be seen/measured
Other components may be made visible with stain (i.e. iodine or ninhydrin) or UV light

## Slide 15: Paper chromatography
Each solute will have a constant retention factor (Rf) for a given eluent.
If two substances have similar Rf values in one solvent, the paper can be turned 90 and eluted with a different solvent for further separation.
  Known as two-way chromatography
  Often used to separate amino acids

## Slide 16: Paper chromatography
Calculating solute retention factors:

## Slide 17: Paper chromatography
You try it… (caluclate the Rf values)

## Slide 18: Thin layer chromatography (TLC)
Similar to paper chromatography
Thin layer of a solid is painted onto an inert support, such as glass
  Common solids:
    Alumina (Al2O3)
    Silica (SiO2)

## Slide 19: Thin layer chromatography (TLC)
When absolutely dry works by adsorption
However, like paper, silica and alumina are very hygroscopic (water-loving) and therefore separation occurs more by partition, with water as the stationary phase.
Separated components can be recovered by scraping off the section containing the component and dissolving it in a suitable solvent.

## Slide 20: Thin layer chromatography (TLC)
Pregnancy tests may use TLC to detect pregnanediol in urine.

## Slide 21: Thin layer chromatography (TLC)
Advantages of TLC over paper chromatography:
  Approx. three times faster
  More efficient – small samples can be separated and components can easily be recovered in pure form
  Results are more easily reproduced
  Range of mixtures can be separated by changing mobile and stationary phases

## Slide 22: Column chromatography
Essentially large-scale TLC
Usually used to separate mixture components for further use rather than simple ID.
Stationary phase often alumina or silical gel (SiO2xH2O)

## Slide 23: Column chromatography
Mixture dissolved in minimum volume of solvent
Added to top of column
Sample is eluted (fresh solvent added to the top to wash sample down the stationary phase)
Components separated as they travel at different rates – collected at bottom as different fractions.
Solvent can also be changed to elute more tightly held components.

## Slide 24: Gas-liquid chromatography (GLC)
Used to separate and ID gases and volatile liquids

## Slide 25: Gas-liquid chromatography (GLC)
Sample injected into oven where it is vaporized
Vapor carried by inert gas (mobile phase) over a non-volatile liquid (stationary phase).
  N2 and He are typical carrier gases
  Long-chain alkanes w/ high b.p.’s supported on a SiO2 (glass) surface typically act as stationary phase

## Slide 26: Gas-liquid chromatography (GLC)
Components generally exit to a flame ionization detector connected to a chart recorder.
The less volatile (lower b.p.) the component, the greater the retention time.

## Slide 27: Gas-liquid chromatography (GLC)
Used to identify components that can vaporize without decomposition
Examples:
  Illegal steroids and stimulants in urine
  Blood-alcohol levels
  Underground mine gases

## Slide 28: Gas chromatography – mass spectrometry (GCMS)
Like GLC, but employs mass spectrometry instead of flame ionization detector at exit point.

## Slide 29: Gas chromatography – mass spectrometry (GCMS)
Computer matches the spectra and gives a printout of all components and their concentrations.
Very powerful tool and used extensively in forensic science, medicine, etc.
Mass spectrometer is connected to a computer which contains a library of the spectra of all known compounds.

## Slide 30: High Performance Liquid Chromatography (HPLC)
Like LC (column chromatography) but employs pressure instead of just gravity to force mobile phase through column.
Stationary phase is typically silica with long-chain alkanes adsorbed to surface,
Efficient separation, so long columns not needed.
sep-pak C18 cartridge
Remember your liquid chromatography lab with grape Kool-Aid?

## Slide 31: High Performance Liquid Chromatography (HPLC)
Separated components often detected via IR spectroscopy.
Like GLC, results recorded onto chart showing different retention times.

## Slide 32: High Performance Liquid Chromatography (HPLC)
Can also be used to separate enantiomers (chiral separation) using columns containing optically active material.
Other uses include analysis of oil pollutants, alcoholic beverages, food (antioxidants, sugars and vitamins), pharmaceuticals, polymers, quality control of insecticides and herbicides.
Can be used for ID as well as for separation